## Slide 1: Cooperative Control and Modeling for Narrow Passage Traversal *with an Ornithopter MAV and Lightweight Ground Station

## Slide 2: Outline
Motivation
Hardware
Cooperative System
System Identification
Model Verification
  Simulation result
  Experimental verification
Conclusions

## Slide 3: Outline
Motivation
Hardware
Cooperative System
System Identification
Model Verification
  Simulation result
  Experimental verification
Conclusions

## Slide 4: Scenario
Want to guide flapping-winged MAV through a window

## Slide 5: Motivation
Mobile robotics platforms can be limited in capabilities at small scales
  Power, size, weight constraints
Cooperation between these systems can allow for completion of objectives that are infeasible for the robots individually

## Slide 6: Goal
Demonstrate the feasibility of cooperation between limited mobile robots to navigate to a common goal
Develop a tracking platform that could be used on a small-scale mobile robot
Develop a model to predict successful navigation
  Achieve simplified model of complex behavior of flapping-winged MAV
    Difficult nonlinear dynamics
    Noisy sensing from flapping movements

## Slide 7: Experimental Setup
Shared global ref frame between camera and robot
Camera tracks location of robot
Ground station computes heading required to reach window
Ground station transmits desired heading to robot
Robot steers to desired heading using on-board controller

## Slide 8: Outline
Motivation
Hardware
Cooperative System
System Identification
Model Verification
  Simulation result
  Experimental verification
Conclusions

## Slide 9: MAV Platform
Built around Silverlit i-Bird RC flyer power train
Tail propeller and servo-controlled elevator for yaw and pitch control
ImageProc 2.4 controller
  40 MIPS microprocessor
  6 DOF IMU
  IEEE 820.15.4 radio
  Motor drivers

## Slide 10: Ground Station Platform
ARM-based BeagleBoard
  OMAP 3530 processor
  128MB RAM
  Consumes 1W power during our experiments
Off-the-shelf USB web camera
  63° viewing triangle
Communicates with IEEE 802.15.4 USB radio module

## Slide 11: Top Level Hardware Interaction

## Slide 12: Outline
Motivation
Hardware
Algorithms
System Identification
Model Verification
  Simulation result
  Experimental verification
Conclusions

## Slide 13: Tracking
Particle filter used to find most likely robot location
  Motion model: Gaussian centered around each particle position with ε-random uniform sampling
  Emission model: motion tracking via background subtraction
Boundary of window selected manually

## Slide 14: Software Control Loop

## Slide 15: Outline
Motivation
Hardware
Cooperative System
System Identification
Model Verification
  Simulation result
  Experimental verification
Conclusions

## Slide 16: System Model
PID Controller
Camera Latency
Transmission Latency
Ground Station
H2Bird
Notes: Same layout, key

## Slide 17: ID Methods

## Slide 18: Outline
Motivation
Hardware
Cooperative System
System Identification
Model Verification
  Simulation result
  Experimental verification
Conclusions

## Slide 19: Experiments
Simulation
  Determine reachable sets for successful window navigation
    Geometrically and in simulation
  Monte Carlo simulation to determine probability of success for given start location
    Each point in 10cm grid, simulate 40 trials of randomly sampled headings from -90° to +90°
Notes: sim

## Slide 20: Model Predicted Feasible Regions

## Slide 21: Model Predicted Feasible Regions

## Slide 22: Model Predicted Feasible Regions

## Slide 23: Model Predicted Feasible Regions

## Slide 24: Experiments
Real-world
  20 trials starting in front of the camera, facing direction of window plane
  60 trials in a 5cm starting grid along edges of view space, facing direction of window plane
Notes: real

## Slide 25: Experimental Results

## Slide 26: Monte Carlo Results

## Slide 27: Outline
Motivation
Hardware
Cooperative System
System Identification
Model Verification
  Simulation result
  Experimental verification
Conclusions

## Slide 28: Conclusions
Model accurate predictor of chance of success at a given start point
  Low computational cost
  Could be used to determine point to begin control to ensure success
A single camera is not sufficient to reliably guide the robot to the goal
  Lack information about the complete pose of the robot

## Slide 29: Future Work
Talk about VLR and multi-view localization method

## Slide 30: Acknowledgements

## Slide 31: References