## Slide 1: Cooperative Control and Modeling for Narrow Passage Traversal *with an Ornithopter MAV and Lightweight Ground Station

## Slide 2: Outline
Motivation
Hardware
Cooperative System
System Identification
Model Verification
  Simulation result
  Experimental verification
Conclusions

## Slide 3: Outline
Motivation
Hardware
Cooperative System
System Identification
Model Verification
  Simulation result
  Experimental verification
Conclusions

## Slide 4: Scenario
Want to guide flapping-winged MAV through a window
MAV requires lightweight electronics
  No visual sensing
Ground station uses camera to track location of MAV
  Sends headings to MAV to guide it to the window

## Slide 5: Motivation
Mobile robotics platforms limited in capabilities at small scales
  Power, size, weight constraints
Cooperation between these systems allows for completion of objectives that are infeasible for the robots individually

## Slide 6: Goal
Demonstrate feasibility of cooperation between limited mobile robots to navigate to a common goal
Develop a tracking platform that could be used on a small-scale mobile robot
Develop a model to predict successful navigation
  Achieve simplified model of complex behavior of flapping-winged MAV
    Difficult nonlinear dynamics
    Noisy sensing from flapping movements

## Slide 7: Experimental Setup
Shared global ref frame between camera and robot
Camera tracks location of robot
Ground station computes heading required to reach window
Ground station transmits desired heading to robot
Robot steers to desired heading using on-board controller

## Slide 8: Outline
Motivation
Hardware
Cooperative System
System Identification
Model Verification
  Simulation result
  Experimental verification
Conclusions

## Slide 9: MAV Platform
Built around Silverlit i-Bird RC flyer power train
Tail propeller and servo-controlled elevator for yaw and pitch control
ImageProc 2.4 controller
  40 MIPS microprocessor
  6 DOF IMU
  IEEE 820.15.4 radio
  Motor drivers

## Slide 10: Ground Station Platform
ARM-based BeagleBoard
  OMAP 3530 processor
  128MB RAM
  Consumes 1W power during our experiments
Off-the-shelf USB web camera
  63° viewing triangle
Communicates with IEEE 802.15.4 USB radio module

## Slide 11: Top Level Hardware Interaction

## Slide 12: Outline
Motivation
Hardware
Algorithms
System Identification
Model Verification
  Simulation result
  Experimental verification
Conclusions

## Slide 13: Tracking
Particle filter used to find most likely robot location
  Motion model: Gaussian centered around each particle position with ε-random uniform sampling
  Emission model: motion tracking via background subtraction
Boundary of window selected manually

## Slide 14: Software Control Loop

## Slide 15: Outline
Motivation
Hardware
Cooperative System
System Identification
Model Verification
  Simulation result
  Experimental verification
Conclusions

## Slide 16: System Model
PID Controller
Camera Latency
Transmission Latency
Ground Station
H2Bird
x,y – H2Bird location in camera frame in pixels
v – H2Bird forward velocity
𝛳 – H2Bird heading
𝛳d – desired H2Bird heading
u – geometrically computed heading input
𝜙 – viewing angle of camera
w – width of camera frame in pixels
Notes: Same layout, key

## Slide 17: Identification Methods
PID Controller
Camera Latency
Transmission Latency
Ground Station
H2Bird
Notes: Same layout, key

## Slide 18: System Model
PID Controller
Camera Latency
Transmission Latency
Ground Station
H2Bird
Transmission latency
  Ping robot from ground station and measure round-trip time
Camera latency
  Point camera at black screen that transitions to white
  Measure time between when screen changes and when camera detects the change
Notes: Same layout, key

## Slide 19: System Model
PID Controller
Camera Latency
Transmission Latency
Ground Station
H2Bird
Control input u determined geometrically
PID controller parameters determined experimentally
Notes: Same layout, key

## Slide 20: Outline
Motivation
Hardware
Cooperative System
System Identification
Model Verification
  Simulation result
  Experimental verification
Conclusions

## Slide 21: Experiments
Simulation
  Determine reachable sets for successful window navigation
    Geometrically and in simulation
  Monte Carlo simulation to determine probability of success for given start location
    Each point in 10cm grid, simulate 40 trials of randomly sampled headings from -90° to +90°
Notes: sim

## Slide 22: Model Predicted Feasible Regions

## Slide 23: Model Predicted Feasible Regions

## Slide 24: Model Predicted Feasible Regions

## Slide 25: Model Predicted Feasible Regions

## Slide 26: Experiments
Real-world
  20 trials starting in front of the camera, facing direction of window plane
  60 trials in a 5cm starting grid along edges of view space, facing direction of window plane
Notes: real

## Slide 27: Experimental Results

## Slide 28: Experiments
Simulation
  Determine reachable sets for successful window navigation
    Geometrically and in simulation
  Monte Carlo simulation to determine probability of success for given start location
    Each point in 10cm grid, simulate 40 trials of randomly sampled headings from -90° to +90°
Notes: sim

## Slide 29: Monte Carlo Results

## Slide 30: Outline
Motivation
Hardware
Cooperative System
System Identification
Model Verification
  Simulation result
  Experimental verification
Conclusions

## Slide 31: Conclusions
Model accurate predictor of chance of success at a given start point
  Low computational cost
  Could be used to determine point to begin control to ensure success
Monocular tracking and control is viable
  Lack information about the complete pose of the robot
  With some modeling can determine regions of high success

## Slide 32: Future Work
Talk about VLR and multi-view localization method

## Slide 33: Acknowledgements

## Slide 34: References